## Slide 1: UbiTap: Leveraging Acoustic Dispersion for Ubiquitous Touch Interface on Solid Surfaces
-Rishika Juloori

## Slide 2: Ubitap
Use a touch screen regardless of time and place, for example, board games
Using touch screens with minimal resources, cutting down on cost and using built-in microphones in regularly used devices.

## Slide 3: Ubitap
Most recent trend! – seamless interaction with various devices using surfaces on objects as touch surfaces.
Many previous works that have focused on tracking user’s fingertip on the surface
Ubitap is an approach that takes on surface touch inputs in a unique way: by listening to the sound, without the loss of portability.
It first records the sound using atleast 3 microphones (in-built). It then analyzes the wave and estimates the location of the sound.

## Slide 4: Requirements of Ubitap
Requirements
Accuracy
Usability
Robustness
Responsiveness
Portability

## Slide 5: Challenges
Variation in surfaces: Touchsound travels with different speeds on different surfaces. Users may use different surfaces depending on the environment.
Relocation of touch input space: possibility to recreate the input for touchsound on a different area of the same surface.
Changes in the surrounding environment: users may place new objects or displace already present objects which may affect reflection patterns

## Slide 6: What’s lacking in current systems?
Low usability and robustness
  Prior works have utilized classification-based techniques
  Accuracy > usability
  Classifications may not be reliable as touchsounds may change depending on the environment.
Low accuracy and portability
  Prior works have utilized TDoA between microphones.
  But accurate measurement of TDoA requires precise hardware with microphones, geophones, accelerometers
  Lower accuracy due to dispersion

## Slide 7: Acoustic Dispersion
A touchsound causes the air pressure around it to change.
Solid surfaces traverses different sound waves (of varying frequencies) at different speeds.
Acoustic dispersion: the idea that different frequency components of the touchsound pass the area near microphones at different times.
Speed of sound on solid surfaces > Speed of sound in air.

## Slide 8: Key Principles
1. Different frequency components of a touchsound propagate at different speeds V(f), where f is their carrying frequency.
2. For a certain surface, V ( f ) is constant regardless of the touch location and the surrounding environment.
3. The TDoA between two different frequency components of a touchsound is linearly proportional to the propagation distance of the touchsound to a microphone (denoted as D), as follows:
-
where is the arrival time of the touchsound at frequency f .

## Slide 9: Ubitap System Architecture

## Slide 10: Ubitap Design
There is an on-surface screen, and
The screen’s size and position relative to the microphones are known in advance.
Touchsounds have an energy level sufficient to analyze
Users have at least three microphones to use a distance-based localization approach

## Slide 11: Touchsound detection
Ubitap uses motion sensors to overcome the problem of noise if a sound-level threshold is used.
It uses energy level of a touch sound which it compares with a threshold to detect the touch

## Slide 12: Arrival time estimation
Ubitap does not use a high-resolution method to detect frequencies as it may compromise responsiveness
It differentiates between high and low frequency waves and deals separately with them.
Low-frequency waves
  Arrive in the form of negative peak
  Highest energy level
High-frequency waves
  Are observed very early => smaller number of samples
  Can use high resolution methods since sample is smaller

## Slide 13: Implementation
This idea requires minimal hardware.
The prototype has been tested on Android running smartphones
Implementation includes capturing raw sensor data using microphones and gyroscopic sensors.
Configurations
  Microphones with sampling rate 192 kHz
  Motion sensors with sampling rate 220 kHz

## Slide 14: Evaluation (set-up)
On-surface touchscreen (36cm X 24cm)
Portable projector (SK Smart Beam)
Microphones of smartphones (2 Google Pixels, 2 Google Pixel XLs)
On a wooden table
Also included glass mirror and acrylic board
Requested the user to tap the calibration points

## Slide 15: Evaluation
Accuracy test
  Overall: Satisfies sub-centimeter accuracy as it captures dispersive characteristics of touchsounds
  Number of microphones: Ubitap provides a great accuracy for greater number of microphones, but has also performed great with the minimal number (3 microphones)

## Slide 16: Evaluation
Robustness test: inputs in dynamic environmental changes
  Changes in position of touchscreen
  Changes in surrounding objects
  Ambient Noise
Responsive test
  Running time of 33.4ms
  Shows it could be useful in variety of applications
Usability test
  Even lower number of calibration points provide higher degree of accuracy
  Prior works trade-off between accuracy and usability

## Slide 17: Potential Limitations
Curvature/irregularity in surfaces
Large obstacles
Smaller display area
Close proximity between microphones
Touch tool variations

## Slide 18: References
Kim Hyosu, Anish Byanjankar, Yunxin Liu, Yuanchao Shu, and Insik Shin. "UbiTap: Leveraging Acoustic Dispersion for Ubiquitous Touch Interface on Solid Surfaces." In Proceedings of ACM Sensys, 2018.